## Slide 1
Implementation & Result
Future work
The Sail RISC-V Model can generate an executable file from its formal specification, and Sail has already been adopted in riscv-arch-test. However, ACT only provides limited test cases and cannot fully validate your RISC-V implementation.
Some chip projects may utilize in-house simulators for testing, yet they fail to obtain the soundness guarantee from formal verification that Sail-RISC-V offers, nor can they match the full configurability of Sail-RISC-V.
We aim to find a more effective method to introduce RISC-V Sail Model into a broader range of testing scenarios.
Pydrofoil is currently bound to a specific commit and requires extensive updates.
Update Sail-RISC-V to provide more common interfaces, such as support for the "skip" functionality.
We have selected the Xiangshan Processor as our test target. It is an open-source RISC-V implementation project that boasts excellent performance, written in Chisel itself. Its source code includes a framework called difftest, and Xiangshan uses NEMU as its test reference. Our goal is to replace NEMU's functionality with a dynamic library based on the Sail model.
This work introduces an approach based on the Pydrofoil framework. Users can develop a series of interfaces suitable for processor testing using simple Python scripts as needed.
This approach leverages both the accuracy of Sail-RISC-V and the high performance of Pydrofoil. Pydrofoil incorporates a suite of compilation optimization techniques, enabling efficient interpretive execution of the Sail-RISC-V model core. Meanwhile, Python-written code is compiled into native C code via PyPy CFFI, without incurring performance overhead.
RISCV Sail Model
Method
An Efficient Approach to Apply the RISC-V Sail Model to Chip Verification
Yanming Zhu¹, Yuxuan Sun¹, Yunxiang Luo¹
¹Programming Language and Compiler Technology Lab
Pydrofoil
Pydrofoil
Extensions
riscv.sail_project
Callbacks
Trap handler
test.elf
Introduction & Motivation
Pydrofoil IR
emulator
System Registers
Model (*.sail)
sail-riscv.ir (jib ir)
RPython Version
sail compiler transform
PyPy Engine
Bind RPython version of the model with Pypy Engine
target cpu implementation
gpr[32]
fpr[32]
vr[32]
mstatus ...
difftest
read_csr
mem_cpy
execute
Workflow
fetch
encdec
execute
Memory State
pc/nextpc
test.elf
Instruction
Instruction
Instruction
Instruction
Instruction
Instruction
Pydrofoil
Difftest serves as the test framework here, responsible for driving the execution of tests. It provides a series of interfaces: first is execute, a function that handles driving test execution; then there are interfaces like read_csr and mem_cpy, which are key interfaces for register comparison and memory comparison.
As a emulator, Sail naturally includes similar function implementations. Therefore, in our Python implementation, we only need to call the corresponding functions such as step, rX_bits, and {read/write}_mem to achieve the corresponding functionality
Compared to implementing a wrapper layer based on C++ or Rust for the sail-model, using Python can significantly reduce boilerplate code and improve development speed. Meanwhile, with the help of CFFI, it can be easily compiled into C without sacrificing performance.
Sail Model
States
Python Implemation
Python Wrapper