## Slide 1
Results
Conclusion
The RISC-V Sail Model can generate an executable simulator from a formal specification, and it has already been used in riscv-arch-test. This work wants to introduce the Sail model into broader verification workflows.
The goal is to keep the model’s semantic accuracy while making integration simple enough for real engineering use. We also want the solution to work with existing test frameworks rather than replacing the whole environment.
The integration process became significantly easier after moving to the pydrofoil based path. The core implementation required only about 800 lines of python code. Most of this code was not about instruction stepping itself; instead, it focused on practical alignment work, especially csr encoding definitions and register-name mapping between sail model and xiangshan. We also added handling for special state elements such as nextpc.
From an engineering perspective, this result supports the original motivation. The adapter remained lightweight, the existing difftest workflow could still be used, and the Sail model could be introduced as a formal-semantic reference without a heavy rewrite of the verification infrastructure. In other words, the method achieved a usable tradeoff among correctness, performance, and implementation effort.
Meanwhile, our experiments also revealed some obvious limitations. Although the Sail model is highly configurable, it currently does not support RVA23. We cannot easily disable certain RVA23 features for Xiangshan, which leads to state consistency issues. After attempting to disable the H extension, we encountered state problems related to PMP, finally stopped when the instruction count reached 894,352.
To achieve this, our methodology is based on pydrofoil, which can be seen as a high-performance execution path for sail-based models and also provide python api. The basic idea is simple: keep the Sail semantic core as the correctness foundation, and use Pydrofoil to make the integration simply and high-performance.
On the integration side, we implement the adapter layer in python with much less boilerplate than a full C++ or rust wrapper. At the same time, the Python code can be compiled through pypy cffi into native C-level artifacts, so this engineering convenience does not necessarily come with large runtime overhead.
We selected xiangshan as the target processor project. Xiangshan is an open-source high-performance RISC-V implementation written in Chisel, and its codebase includes a difftest framework that traditionally uses NEMU as the reference model. Our goal is to replace NEMU with a sail-based dynamic library while preserving the existing difftest workflow as much as possible.
Method
An Efficient Approach to Apply the RISC-V Sail Model to Chip Verification
Yanming Zhu1, Yunxiang Luo¹
1Intelligent Software Research Center, Institute of Software, Chinese Academy of Sciences
Motivation
target cpu implementation
gpr[32]
fpr[32]
vr[32]
mstatus ...
difftest
read_csr
mem_cpy
execute
Workflow
fetch
encdec
execute
Memory State
pc/nextpc
test.elf
Instruction
Instruction
Instruction
Instruction
Instruction
Instruction
Pydrofoil
This work presents a practical way to apply the RISC-V Sail model to chip verification by combining Sail semantics, pydrofoil performance, and a lightweight python + cffi adapter. The approach keeps the existing difftest structure largely intact and reduces integration complexity, while preserving the core advantage of a formally grounded reference model.
The experiments also show that future progress depends on toolchain maturity and feature alignment. Pydrofoil is currently tied to a specific commit and still needs substantial updates. Moving to newer versions with broader extension support and more common interfaces is necessary for deeper experimentation and wider adoption.
Sail Model
States
Python Implemation
Python Wrapper
sail-riscv
pydrofoil
source